FORD RANGER Raptor Specifications

CHASSIS

| Suspension | Front – Independent SLA with aluminium arms, featuring FOX 2.5-inch internal bypass shock absorbers with Position Sensitive Damping |
| --- | --- |
|  | Rear – Multilink solid rear axle with Watt’s Link featuring FOX 2.5-inch internal bypass shock absorbers with Position Sensitive Damping |
| Steering | Rack and pinion with Electric Power Assisted Steering (EPAS) |
|  | Ratio – 18.6:1 |
|  | Turning circle (kerb-to-kerb) – 12.9 m |
|  | Turns lock-to-lock – 3.49 |
| Brakes | Front – ventilated discs 332 x 32 mm |
|  | Rear – ventilated discs 332 x 24 mm |
|  | Modulation – Electronic Brakeforce Distribution; Electronic four-channel anti-lock braking system with Electronic Stability Control; Emergency Brake Assist; Hill Descent Control; Hill Start Assist; Load Adaptive Control; Pre-Collision Assist with Pedestrian Detection; Roll Over Mitigation; Trailer Sway Control |
| Wheels & tyres | 8.5 x 17-inch alloy wheels | 285/70 R17 BFGoodrich All-Terrain T/A KO2 |

POWERTRAIN

| Engine | 2.0-litre EcoBlue Bi-turbo diesel |
| --- | --- |
| Type | In-line four-cylinder turbodiesel, longitudinal |
| Capacity (cc) | 1996 |
| Bore (mm) | 84.01 |
| Stroke (mm) | 90.00 |
| Max power (PS / kW) | 213 / 157 |
| At engine speed (rpm) | 3750 |
| Max torque (Nm) | 500 |
| At engine speed (rpm) | 1750-2000 |
| Comp. ratio | 16:0:1 |
| Cylinder block | Cast iron, offset cylinder bores |
| Cylinder head | Cast aluminium alloy, integrated intake manifold, integrated high-pressure EGR passage |
| Camshaft drive | Belt-in-oil camshaft drive with automatic tensioner driven off an idler gear driven from crankshaft |
| Crankshaft | Steel forging with induction-hardened bearing surfaces, 4 counter-weights, 5 main bearings |
| Cylinders | 4 in-line |
| Valve gear | DOHC with 4 valves per cylinder, hydraulic lash adjusters, roller-finger followers |
| Turbocharger | Bi-turbo series sequential system, high-pressure variable geometry turbo, low-pressure stage fixed geometry turbo with vacuum-activated wastegate, passive compressor bypass valve. Active turbine bypass valve, vacuum actuated. Intercooler using air-cooled air charger |
| Lubrication system | Pressure-fed lubrication system, single-stage variable-displacement oil pump |
| System capacity | Initial factory fill – 8 litres, service oil fill (with oil filter) – 7.12 litres |
| Water pump | Mechanical drive, thermostat with integrated engine coolant temperature sensor |
| System capacity | 12 litres including heater |
| Engine Management | Bosch FDEC |
| Fuel injection | Direct-injection, high-pressure common rail, piezo injectors |
| Emission controls | Selective Catalytic Reduction (SCR) with urea injection oxidation catalyst and standard catalysed diesel particulate filter (cDPF). Water-cooled, high-pressure exhaust gas recirculation (EGR) with bypass |
| Emission level | Euro Stage 6 |
| Transmission | 10-speed automatic |
| Gear ratios |  |
| 10th 9th 8th 7th 6th 5th 4th 3rd 2nd 1st Reverse | 0.636 0.689 0.854 1.000 1.275 1.520 1.769 2.146 2.985 4.696 4.866 |
| Final Drive | 3.73:1 |
| High range | 1:1 |
| Low range | 2.72:1 |

4X4 DRIVELINE

| Type | Driver-selectable four-wheel drive with electronically controlled transfer box offering: Rear-wheel drive high-range (2H) Four-wheel drive high-range (4H) Four-wheel drive low-range (4L) |
| --- | --- |
| 4x4 Transfer box | Electronic Shift-on-the-Fly, part-time 4x4 transfer case |
| Terrain Management System | Six Selectable Drive Modes: Normal, Sport, Grass/Gravel, Snow, Mud/Sand, Baja, Rock |

DIMENSIONS AND CAPACITIES

| Exterior (mm) |  |
| --- | --- |
| Overall length with / without towbar | 5374 / 5363 |
| Overall width (inc mirrors) | 2180 |
| Overall width (excl mirrors) | 2028 |
| Overall height | 1873 |
| Wheelbase | 3220 |
| Ground clearance (unladen) | 283 |
| Wading depth | 850 |
| Front track | 1710 |
| Rear track | 1710 |
| Front overhang | 908 |
| Rear overhang with / without towbar | 1246 /1235 |
| Angles (deg.) |  |
| Approach angle | 32.5° |
| Departure angle with / without towbar | 24 / 27° |
| Ramp / Breakover angle | 25° / 24° |
| Interior first row (mm) |  |
| Front headroom | 1022 |
| Max. leg room | 1116 |
| Shoulder room | 1355 |
| Interior second row (mm) |  |
| Headroom | 986 |
| Max. legroom | 902 |
| Knee clearance | 39 |
| Shoulder room | 1432 |
| Cargo Bed (mm) |  |
| Width | 1560 |
| Width between arches | 1139 |
| Length | 1575 |
| Depth | 561 |
| Cargo floor height to ground kerb | 906 |
| Rear opening width | 1330 |
| Fuel tank capacity (litres) | 80 |

WEIGHTS

|  | Minimum kerbweight (kg) | Gross Vehicle Mass (kg) | Maximum Gross Payload (kg) | Max. towable mass (braked) (kg) | Max towable mass (unbraked) (kg) |
| --- | --- | --- | --- | --- | --- |
| Ford Ranger Raptor | 2510 | 3130 | 620 | 2500 | 750 |

Minimum kerbweight represents the lightest kerbweight including full fluid levels and 90 per cent fuel levels, subject to manufacturing tolerances and options. Towing limits quoted represent the maximum braked towing capacity of the vehicle on a 12 per cent gradient at sea level. The performance and economy will be reduced when used for towing.

ECONOMY, PERFORMANCE AND EMISSIONS

|  |  | Fuel consumption l/100 km (mpg)* | PerformanceØ |
| --- | --- | --- | --- |
|  | CO2 (g/km) | Urban | Extra Urban | Combined | Max. speed km/h (mph) | 0-100 km/h (0-62 mph) secs |
| Ford Ranger Raptor 2.0-litre EcoBlue, 10-speed automatic | 233 | 10.6 (26.6) | 8.0 (35.3) | 8.9 (31.7) | 170 (106) | 10.5 |

ØFord test figures.

# # #

Note: The data information in this press release reflects preliminary specifications and was correct at the time of going to print. However, Ford policy is one of continuous product improvement. The right is reserved to change these details at any time.

*The declared fuel/energy consumptions, CO2 emissions and electric range are measured according to the technical requirements and specifications of the European Regulations (EC) 715/2007 and (EC) 692/2008 as last amended. Fuel consumption and CO2 emissions are specified for a vehicle variant and not for a single car. The applied standard test procedure enables comparison between different vehicle types and different manufacturers. In addition to the fuel-efficiency of a car, driving behaviour as well as other non-technical factors play a role in determining a car's fuel/energy consumption, CO2 emissions and electric range. CO2 is the main greenhouse gas responsible for global warming.

Since 1 September 2017, certain new vehicles are being type-approved using the World Harmonised Light Vehicle Test Procedure (WLTP) according to (EU) 2017/1151 as last amended, which is a new, more realistic test procedure for measuring fuel consumption and CO2 emissions. Since 1 September 2018 the WLTP has begun replacing the New European Drive Cycle (NEDC), which is the outgoing test procedure. During NEDC Phase-out, WLTP fuel consumption and CO2 emissions are being correlated back to NEDC. There will be some variance to the previous fuel economy and emissions as some elements of the tests have altered i.e., the same car might have different fuel consumption and CO2 emissions.

About Ford Motor Company

Ford Motor Company is a global company based in Dearborn, Michigan. The company designs, manufactures, markets and services a full line of Ford cars, trucks, SUVs, electrified vehicles and Lincoln luxury vehicles, provides financial services through Ford Motor Credit Company and is pursuing leadership positions in electrification, autonomous vehicles and mobility solutions. Ford employs approximately 199,000 people worldwide. For more information regarding Ford, its products and Ford Motor Credit Company, please visit www.corporate.ford.com.

Ford of Europe is responsible for producing, selling and servicing Ford brand vehicles in 50 individual markets and employs approximately 53,000 employees at its wholly owned facilities and approximately 67,000 people when joint ventures and unconsolidated businesses are included. In addition to Ford Motor Credit Company, Ford Europe operations include Ford Customer Service Division and 24 manufacturing facilities (16 wholly owned or consolidated joint venture facilities and eight unconsolidated joint venture facilities). The first Ford cars were shipped to Europe in 1903 – the same year Ford Motor Company was founded. European production started in 1911.

Contact: Peter Watt Ford of Europe +44 (0) 1268 401 307 pwatt3@ford.com