Technical Specifications

| MAZDA CX-30 |
| --- |
| Body type | Monocoque |
| Doors | 4 + liftgate |
| Seating capacity | 5 |
| External |
| Overall length (with licence plate holder) | mm | 4,395 |
| Overall width (with wheel arch molding) | mm | 1,795 |
| Overall width (mirror to mirror ) | mm | 2,040 |
| Overall height (unladen, without sharkfin antenna) | mm | 1,540 |
| Wheelbase | mm | 2,655 |
| Overhang front (with licence plate holder) | mm | 915 |
| Overhang rear | mm | 825 |
| Tread front | mm | 1,565 |
| Tread rear | mm | 1,565 |
| Ground clearance between axles (laden, w. 75kg driver) | mm | 175 |
| Interior |
| Front headroom | mm | 967 |
| Rear headroom | mm | 973 |
| Front shoulder room | mm | 1412 |
| Rear shoulder room | mm | 1361 |
| Front hip room | mm | 1388 |
| Rear hip room | mm | 1352 |
| Rear legroom | mm | 921 |
| Boot |
| Volume with rear seats up VDA (with under floor storage) | l | 430 (422 with Bose) |
| Volume to roof, rear seats folded down (VDA) | l | 1,406 (1398 with Bose) |
| Height, from floor to tonneau cover | mm | 570 (525 with Bose) |
| Load floor length to 2nd row | mm | 809 |
| Loading sillheight from ground | mm | 533 |
| Liftgate opening width | mm | 1,030 |

Engine line-up

|  | SKYACTIV-G 2.0 (122 PS) | SKYACTIV-D 1.8 (116 PS) |
| --- | --- | --- |
| Powertrain | FWD | AWD | FWD | AWD |
| Transmission | 6MT | 6AT | 6MT | 6AT | 6MT | 6AT | 6MT | 6AT |
| Engine type | I4 DOHC 16 valves | I4 DOHC 16 valves |
| Displacement | cm3 | 1,998 | 1,759 |
| Bore x stroke | 83.5 x 91.2 | 79.0 x 89.7 |
| Fuel injection type | Direct injection | Direct injection |
| Compression ratio | 13 | 14,8 |
| Emission control system | Three-way catalyst | Oxidation catalyst & NSC & DPF |
| Max. power | kW (PS)/ rpm | 90 (122)/6000 | 85 (116)/4000 |
| Max. torque | Nm/ rpm | 213/4000 | 270/1600-2600 |
| Recommended fuel type | 95 RON | Diesel |
| Fuel tank capacity | l | 51 | 48 | 51 | 48 |

Mazda M Hybrid

|  | SKYACTIV-G 2.0 (122 PS) |
| --- | --- |
| Hybrid type | Belt-driven integrated starter generator (B-ISG) |
| Lithium-ion battery capacity | kJ | 600 |
| Voltage | V | 24 Volt mild hybrid |
| DC/DC converter | kW | 1.7 (max 120A) |

Manual Transmission: Skyactiv-MT

|  | SKYACTIV-G 2.0 (122 PS) | SKYACTIV-D 1.8 (116 PS) |
| --- | --- | --- |
| Transmission | 6MT | 6MT |
| Powertrain | FWD | AWD | FWD | AWD |
| Gear ratios |
| 1st | 3.700 | 3.700 | 3.700 | 3.700 |
| 2nd | 1.947 | 1.947 | 1.947 | 1.947 |
| 3rd | 1.300 | 1.300 | 1.300 | 1.300 |
| 4th | 1.029 | 1.029 | 0.916 | 0.916 |
| 5th | 0.837 | 0.837 | 0.717 | 0.717 |
| 6th | 0.680 | 0.680 | 0.580 | 0.580 |
| Reverse | 3.724 | 3.724 | 3.724 | 3.724 |
| Final drive ratio | 3.850 | 4.105 | 4.105 | 4.105 |

Automatic Transmission: Skyactiv-Drive

|  | SKYACTIV-G 2.0 (122 PS) | SKYACTIV-D 1.8 (116 PS) |
| --- | --- | --- |
| Transmission | 6AT | 6AT |
| Powertrain | FWD | AWD | FWD | AWD |
| Gear ratios |
| 1st | 3.552 | 3.552 | 3.552 | 3.552 |
| 2nd | 2.022 | 2.022 | 2.022 | 2.022 |
| 3rd | 1.347 | 1.347 | 1.347 | 1.347 |
| 4th | 1.000 | 1.000 | 1.000 | 1.000 |
| 5th | 0.745 | 0.745 | 0.745 | 0.745 |
| 6th | 0.599 | 0.599 | 0.599 | 0.599 |
| Reverse | 3.052 | 3.052 | 3.052 | 3.052 |
| Final drive ratio | 4.095 | 4.367 | 4.367 | 4.367 |

Suspension and wheels

|  | SKYACTIV-G 2.0 (122 PS) | SKYACTIV-D 1.8 (116 PS) |
| --- | --- | --- |
| Suspension |
| Front suspension | MacPherson strut |
| Rear suspension | Torsion Beam |
| Wheel & Tyres |
| Wheel size | 16x6-1/2J 18X7J |
| Tyre size | 215/65R16 215/55R18 |

Steering and brakes

|  | SKYACTIV-G 2.0 (122 PS) | SKYACTIV-D 1.8 (116 PS) |
| --- | --- | --- |
| Steering |
| Steering type |  | Rack and pinion |
| Power assist type |  | Electric Power Assisted Steering (EPAS) |
| Turning circle radius (kerb to kerb) | m | 5.3 |
| Turning circle diameter (wall to wall) | m | 11.37 |
| Brakes |
| Type front |  | Ventilated discs |
| Type rear |  | Solid discs |
| Diameter front | mm | 295 |
| Diameter rear | mm | 265 |

Weight and payload

|  | SKYACTIV-G 2.0 (122 PS) | SKYACTIV-D 1.8 (116 PS) |
| --- | --- | --- |
| Transmission | 6MT | 6AT | 6MT | 6AT |
| Powertrain | FWD | AWD | FWD | AWD | FWD | AWD | FWD | AWD |
| Min. kerb weight | kg | 1,320 | 1,404 | 1,347 | 1,430 | 1,344 | 1,424 | 1,371 | 1,447 |
| Max. Permissible weight (GVW) | kg | 1,927 | 1,995 | 1,957 | 2,021 | 1,949 | 2,013 | 1,969 | 2,033 |
| Permissible front axle weight | kg | 1,020 | 1,060 | 1,052 | 1,092 | 1,074 | 1,094 | 1,096 | 1,116 |
| Permissible rear axle weight | kg | 982 | 1,010 | 980 | 1,004 | 950 | 994 | 948 | 992 |
| Permissible tow weight, trailer without brakes | kg | 600 | 600 | 600 | 600 | 600 | 600 | 600 | 600 |
| Permissible tow weight, trailer with brakes (8%/12% gradient) | kg | 1,300 | 1,300 | 1,300 | 1,300 | 1,300 | 1,300 | 1,300 | 1,300 |
| Max. roof load capacity | kg | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 |

Performance

|  | SKYACTIV-G 2.0 (122 PS) | SKYACTIV-D 1.8 (116 PS) |
| --- | --- | --- |
| Transmission | 6MT | 6AT | 6MT | 6AT |
| Powertrain | FWD | AWD | FWD | AWD | FWD | AWD | FWD | AWD |
| Performance |
| Top speed (w. limiter) Under Mazda test conditions. | km/h |  | 186 | 182 | 186 | 182 | 183 | 179 | 183 | 179 |
| Acceleration (0-100km/h)1 | secs. |  | 10,6 | 11,1 | 11,2 | 11,7 | 10,8 | 11,6 | 12,6 | 13,5 |
| WLTP fuel consumption Vehicles are homologated in accordance with the type approval procedure WLTP (Regulation (EU) 1151 / 2017; Regulation (EU) 2007/715). |
| Combined | l/100 km | 16inch 18inch | 6,2 | 6,8 | 6,6 | 7,3 | 5,1 | 5,7 | 6,0 | 6,6 |
| Extra-High | l/100 km | 16inch 18inch | 6,5 | 6,8 | 6,9 | 7,6 | 6,2 | 6,7 | 6,7 | 7,2 |
| High | l/100 km | 16inch 18inch | 5,3 | 5,9 | 5,5 | 6,1 | 4,1 | 5,0 | 5,0 | 5,7 |
| Medium | l/100 km | 16inch 18inch | 5,9 | 6,8 | 6,3 | 7,0 | 4,8 | 5,3 | 5,9 | 6,5 |
| Low | l/100 km | 16inch 18inch | 8,0 | 9,0 | 8,7 | 9,7 | 4,9 | 5,3 | 6,6 | 7,3 |
| CO2 emissions (combined) | g/km | 16inch 18inch | 141 | 153 | 151 | 165 | 135 | 150 | 158 | 173 |
| NEDC fuel consumption To provide comparability the referred values are NEDC – values determined in line with Implementation Regulation (EU) 1153 / 2017. |
| Combined | l/100 km | 16inch 18inch | 5,1 | 5,3 | 5,5 | 6,0 | 4,4 | 4,7 | 5,0 | 5,2 |
| Extra Urban | l/100 km | 16inch 18inch | 4,5 | 4,7 | 4,8 | 5,3 | 4,1 | 4,5 | 4,8 | 5,0 |
| Urban | l/100 km | 16inch 18inch | 6,2 | 6,4 | 6,8 | 7,3 | 5,1 | 4,9 | 5,2 | 5,6 |
| CO2 emissions (combined) | g/km | 16inch 18inch | 116 | 121 | 126 | 136 | 116 | 122 | 129 | 137 |
| Emissions rating | Euro 6d | Euro 6d-TEMP |