Mercedes-Benz V-Class 220 d

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 120 (163)/4,200 |
| Rated torque | Nm at rpm | 380/1,200-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | Rear-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 16 - 8 J x 19 |
| Tyres | 205/65 R 16 - 245/45 R 19 |

Dimensions and weights

|  |  | Compact | Long | Extra long |
| --- | --- | --- | --- | --- |
| Wheelbase | mm | 3,200 | 3,200 | 3,430 |
| Track front/rear | mm | 1,666/1,646 | 1,666/1,646 | 1,666/1,646 |
| Length | mm | 4,895 | 5,140 | 5,370 |
| Width | mm | 1,928 | 1,928 | 1,928 |
| Height | mm | 1,880 | 1,880 | 1,880 |
| Kerb weight | kg | 2,127 | 2,152 | 2,177 |
| Payload | kg | 973-1,063 | 948-1,038 | 923-1,013 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 | 3,100; 3,200 | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 | 750/2,000, 2,500 | 750/2,000; 2,500 |
| Turning circle | m | 11.8 | 11.8 | 12.5 |
| Tank capacity and reserve | L | 57/10 | 57/10 | 57/10 |
| AdBlue® tank | l | 24 | 24 | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 11 | 11.1 | 11.2 |
| --- | --- | --- | --- | --- |
| Top speed | km/h | 195 | 195 | 195 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 6.2/ 5.9/ 6.0 | 6.4-6.2/ 6.0-5.9/ 6.2-6.0 | 6.2 / 5.9/ 6.0 |
| Efficiency class |  | A | A | A |
| CO2 emissions comb.1 | g/km | 157 | 162-157 | 158-157 |

Mercedes-Benz V-Class 220 d 4MATIC

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 120 (163)/4,200 |
| Rated torque | Nm at rpm | 380/1,200-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | All-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

|  |  | Compact | Long |  |
| --- | --- | --- | --- | --- |
| Wheelbase | mm | 3,200 | 3,200 |  |
| Track front/rear | mm | 1,670/1,650 | 1,670/1,650 |  |
| Length | mm | 4,895 | 5,140 |  |
| Width | mm | 1,928 | 1,928 |  |
| Height | mm | 1,880 | 1,880 |  |
| Kerb weight | kg | 2,195 | 2,220 |  |
| Payload | kg | 905-995 | 880-970 |  |
| Permissible gross vehicle weight | kg | 3,100; 3,200 | 3,100; 3,200 |  |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 | 750/2,000; 2,500 |  |
| Turning circle | m | 13.1 | 13.1 |  |
| Tank capacity and reserve | l | 57/10 | 57/10 |  |
| AdBlue® tank | l | 24 | 24 |  |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 12.1 | 12.3 |  |
| --- | --- | --- | --- | --- |
| Top speed | km/h | 188 | 188 |  |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 7.1-7.0/ 6.6-6.5/ 6.7 | 7.3-7.0/ 6.8-6.5/ 6.9-6.7 |  |
| Efficiency class |  | B | B |  |
| CO2 emissions comb.1 | g/km | 178-176 | 184-177 |  |

Mercedes-Benz V-Class 250 d

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 140 (190)/4,200 |
| Rated torque | Nm at rpm | 440/1,350-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | Rear-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

|  |  | Compact | Long | Extra long |
| --- | --- | --- | --- | --- |
| Wheelbase | mm | 3,200 | 3,200 | 3,430 |
| Track front/rear | mm | 1,666/1,646 | 1,666/1,646 | 1,666/1,646 |
| Length | mm | 4,895 | 5,140 | 5,370 |
| Width | mm | 1,928 | 1,928 | 1,928 |
| Height | mm | 1,880 | 1,880 | 1,880 |
| Kerb weight | kg | 2,127 | 2,152 | 2,177 |
| Payload | kg | 973-1,063 | 948-1,038 | 923-1,013 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 | 3,100; 3,200 | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 | 750/2,000; 2,500 | 750/2,000, 2,500 |
| Turning circle | m | 11.8 | 11.8 | 12.5 |
| Tank capacity and reserve | l | 57/10 | 57/10 | 57/10 |
| AdBlue® tank | l | 24 | 24 | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 9.4 | 9.5 | 9.6 |
| --- | --- | --- | --- | --- |
| Top speed | km/h | 205 | 205 | 205 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 6.5-6.4/ 5.6/ 5.9 | 6.7-6.4/ 5.7-5.6/ 6.1-5.9 | 6.6-6.4/ 5.6/ 6.0-5.9 |
| Efficiency class |  | A | A | A |
| CO2 emissions comb.1 | g/km | 156-155 | 161-155 | 158-156 |

Mercedes-Benz V-Class 250 d 4MATIC

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 140 (190)/4,200 |
| Rated torque | Nm at rpm | 440/1,350-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | All-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

|  |  | Compact | Long |  |
| --- | --- | --- | --- | --- |
| Wheelbase | mm | 3,200 | 3,200 |  |
| Track front/rear | mm | 1,670/1,650 | 1,670/1,650 |  |
| Length | mm | 4,895 | 5,140 |  |
| Width | mm | 1,928 | 1,928 |  |
| Height | mm | 1,880 | 1,880 |  |
| Kerb weight | kg | 2,195 | 2,220 |  |
| Payload | kg | 905-995 | 880-970 |  |
| Permissible gross vehicle weight | kg | 3,100; 3,200 | 3,100; 3,200 |  |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000, 2,500 | 750/2,000, 2,500 |  |
| Turning circle | m | 13.1 | 13.1 |  |
| Tank capacity and reserve | l | 57/10 | 57/10 |  |
| AdBlue® tank | l | 24 | 24 |  |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 10.3 | 10.5 |  |
| --- | --- | --- | --- | --- |
| Top speed | km/h | 199 | 199 |  |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 7.4-7.3/ 6.2-6.1/ 6.6-6.5 | 7.6-7.3/ 6.3-6.1/ 6.8-6.5 |  |
| Efficiency class |  | B | B |  |
| CO2 emissions comb.1 | g/km | 173-172 | 179-172 |  |

Mercedes-Benz V-Class 300 d

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 176 (239)/4,200 |
| Rated torque | Nm at rpm | 500 (+30)4/1,600-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | Rear-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4,8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

|  |  | Compact | Long | Extra long |
| --- | --- | --- | --- | --- |
| Wheelbase | mm | 3,200 | 3,200 | 3,430 |
| Track front/rear | mm | 1,666/1,646 | 1,666/1,646 | 1,666/1,646 |
| Length | mm | 4,895 | 5,140 | 5,370 |
| Width | mm | 1,928 | 1,928 | 1,928 |
| Height | mm | 1,880 | 1,880 | 1,880 |
| Kerb weight | kg | 2,127 | 2,152 | 2,177 |
| Payload | kg | 973-1,063 | 948-1,038 | 923-1,013 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 | 3,100, 3,200 | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 | 750/2,000; 2,500 | 750/2,000; 2,500 |
| Turning circle | m | 11.8 | 11.8 | 12.5 |
| Tank capacity and reserve | l | 57/10 | 57/10 | 57/10 |
| AdBlue® tank | l | 24 | 24 | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 7.8 | 7.9 | 7.9 |
| --- | --- | --- | --- | --- |
| Top speed | km/h | 220 | 220 | 220 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 6.5-6.4/ 5.6/ 5.9 | 6.7-6.4/ 5.7-5.6/ 6.1-5.9 | 6.6-6.4/ 5.6/ 6.0-5.9 |
| Efficiency class |  | A | A | A |
| CO2 emissions comb.1 | g/km | 156-155 | 161-155 | 158-156 |

Mercedes-Benz V-Class 300 d 4MATIC

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 176 (239)/4,200 |
| Rated torque | Nm at rpm | 500 (+30)4/1,600-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | All-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

|  |  | Compact | Long |  |
| --- | --- | --- | --- | --- |
| Wheelbase | mm | 3,200 | 3,200 |  |
| Track front/rear | mm | 1,670/1,650 | 1,670/1,650 |  |
| Length | mm | 4,895 | 5,140 |  |
| Width | mm | 1,928 | 1,928 |  |
| Height | mm | 1,880 | 1,880 |  |
| Kerb weight | kg | 2,195 | 2,220 |  |
| Payload | kg | 905-995 | 880-970 |  |
| Permissible gross vehicle weight | kg | 3,100; 3,200 | 3,100; 3,200 |  |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 | 750/2,000; 2.500 |  |
| Turning circle | m | 13.1 | 13.1 |  |
| Tank capacity and reserve | l | 57/10 | 57/10 |  |
| AdBlue® tank | l | 24 | 24 |  |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 8.5 | 8.6 |  |
| --- | --- | --- | --- | --- |
| Top speed | km/h | 214 | 214 |  |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 7.4-7.3/ 6.2-6.1/ 6.6-6.5 | 7.6-7.3/ 6.3-6.1/ 6.8-6.5 |  |
| Efficiency class |  | B | B |  |
| CO2 emissions comb.1 | g/km | 173-172 | 179-172 |  |

Mercedes-Benz Marco Polo 220 d

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 120 (163)/4,200 |
| Rated torque | Nm at rpm | 380/1,200-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | Rear-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 16 - 8 J x 19 |
| Tyres | 205/65 R 16 - 245/45 R 19 |

Dimensions and weights

| Wheelbase | mm | 3,200 |
| --- | --- | --- |
| Track front/rear | mm | 1,666/1,646 |
| Length | mm | 5,140 |
| Width | mm | 1,928 |
| Height | mm | 1,980 |
| Kerb weight | kg | 2,487 |
| Payload | kg | 613-703 |
| Permissible gross vehicle weight | kg | 3,100, 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 |
| Turning circle | m | 11.8 |
| Tank capacity and reserve | l | 57/10 |
| AdBlue® tank | l | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 12.3 |
| --- | --- | --- |
| Top speed | km/h | 192 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 6.4/ 6.1/ 6.2 |
| Efficiency class |  | A+ |
| CO2 emissions comb.1 | g/km | 163-162 |

Mercedes-Benz Marco Polo 220 d 4MATIC

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 120 (163)/4,200 |
| Rated torque | Nm at rpm | 380/1,200-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | All-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

| Wheelbase | mm | 3,200 |
| --- | --- | --- |
| Track front/rear | mm | 1,670/1,650 |
| Length | mm | 5,140 |
| Width | mm | 1,928 |
| Height | mm | 1,980 |
| Kerb weight | kg | 2,555 |
| Payload | kg | 545-635 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 |
| Turning circle | m | 13.1 |
| Tank capacity and reserve | l | 57/10 |
| AdBlue® tank | l | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 13.7 |
| --- | --- | --- |
| Top speed | km/h | 185 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 7.2/ 6.7/ 6.9 |
| Efficiency class |  | A |
| CO2 emissions comb.1 | g/km | 182-181 |

Mercedes-Benz Marco Polo 250 d

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 140 (190)/4,200 |
| Rated torque | Nm at rpm | 440/1,350-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | Rear-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

| Wheelbase | mm | 3,200 |
| --- | --- | --- |
| Track front/rear | mm | 1,666/1,646 |
| Length | mm | 5,140 |
| Width | mm | 1,928 |
| Height | mm | 1,980 |
| Kerb weight | kg | 2,487 |
| Payload | kg | 613-703 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 |
| Turning circle | m | 11.8 |
| Tank capacity and reserve | l | 57/10 |
| AdBlue® tank | l | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 10.4-10.5 |
| --- | --- | --- |
| Top speed | km/h | 203 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 6.8-6.7/ 5.7/ 6.1 |
| Efficiency class |  | A+ |
| CO2 emissions comb.1 | g/km | 162-161 |

Mercedes-Benz Marco Polo 250 d 4MATIC

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 140 (190)/4,200 |
| Rated torque | Nm at rpm | 440/1,350-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | All-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

| Wheelbase | mm | 3,200 |
| --- | --- | --- |
| Track front/rear | mm | 1,670/1,650 |
| Length | mm | 5,140 |
| Width | mm | 1,928 |
| Height | mm | 1,980 |
| Kerb weight | kg | 2,555 |
| Payload | kg | 545-635 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 |
| Turning circle | m | 13.1 |
| Tank capacity and reserve | l | 57/10 |
| AdBlue® tank | l | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 11.6 |
| --- | --- | --- |
| Top speed | km/h | 196 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 7.5/ 6.3/ 6.7 |
| Efficiency class |  | A |
| CO2 emissions comb.1 | g/km | 177-176 |

Mercedes-Benz Marco Polo 300 d

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 176 (239)/4,200 |
| Rated torque | Nm at rpm | 500 (+30)4/1,600-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | Rear-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

| Wheelbase | mm | 3,200 |
| --- | --- | --- |
| Track front/rear | mm | 1,666/1,646 |
| Length | mm | 5,140 |
| Width | mm | 1,928 |
| Height | mm | 1,980 |
| Kerb weight | kg | 2,487 |
| Payload | kg | 613-703 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 |
| Turning circle | m | 11.8 |
| Tank capacity and reserve | l | 57/10 |
| AdBlue® tank | l | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 8.6 |
| --- | --- | --- |
| Top speed | km/h | 215 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 6.8-6.7/ 5.7/ 6.1 |
| Efficiency class |  | A+ |
| CO2 emissions comb.1 | g/km | 162-161 |

Mercedes-Benz Marco Polo 300 d 4MATIC

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 176 (239)/4,200 |
| Rated torque | Nm at rpm | 500 (+30)4/1,600-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | All-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

| Wheelbase | mm | 3,200 |
| --- | --- | --- |
| Track front/rear | mm | 1,670/1,650 |
| Length | mm | 5,140 |
| Width | mm | 1,928 |
| Height | mm | 1,980 |
| Kerb weight | kg | 2,555 |
| Payload | kg | 545-635 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 |
| Turning circle | m | 13.1 |
| Tank capacity and reserve | l | 57/10 |
| AdBlue® tank | l | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 9.4 |
| --- | --- | --- |
| Top speed | km/h | 210 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 7.5/ 6.3/ 6.7 |
| Efficiency class |  | A |
| CO2 emissions comb.1 | g/km | 177-176 |

Mercedes-Benz Marco Polo HORIZON 220 d

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 120 (163)/4,200 |
| Rated torque | Nm at rpm | 380/1,200-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | Rear-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 16 - 8 J x 19 |
| Tyres | 205/65 R 16 - 245/45 R 19 |

Dimensions and weights

| Wheelbase | mm | 3,200 |
| --- | --- | --- |
| Track front/rear | mm | 1,666/1,646 |
| Length | mm | 5,140 |
| Width | mm | 1,928 |
| Height | mm | 1,995 |
| Kerb weight | kg | 2,377 |
| Payload | kg | 723-813 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 |
| Turning circle | m | 11.8 |
| Tank capacity and reserve | l | 57/10 |
| AdBlue® tank | l | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 11.9 |
| --- | --- | --- |
| Top speed | km/h | 192 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 6.3/ 6.0/ 6.1 |
| Efficiency class |  | A |
| CO2 emissions comb.1 | g/km | 161 |

Mercedes-Benz Marco Polo HORIZON 220 d 4MATIC

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 120 (163)/4,200 |
| Rated torque | Nm at rpm | 380/1,200-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | All-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

| Wheelbase | mm | 3,200 |
| --- | --- | --- |
| Track front/rear | mm | 1,670/1,650 |
| Length | mm | 5,140 |
| Width | mm | 1,928 |
| Height | mm | 1,995 |
| Kerb weight | kg | 2,445 |
| Payload | kg | 655-745 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2.500 |
| Turning circle | m | 13.1 |
| Tank capacity and reserve | l | 57/10 |
| AdBlue® tank | l | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 13.1-13.2 |
| --- | --- | --- |
| Top speed | km/h | 186 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 7.1/ 6.7-6.6/ 6.8 |
| Efficiency class |  | A |
| CO2 emissions comb.1 | g/km | 180 |

Mercedes-Benz Marco Polo HORIZON 250 d

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 140 (190)/4,200 |
| Rated torque | Nm at rpm | 440/1,350-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | Rear-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

| Wheelbase | mm | 3,200 |
| --- | --- | --- |
| Track front/rear | mm | 1,666/1,646 |
| Length | mm | 5,140 |
| Width | mm | 1,928 |
| Height | mm | 1,995 |
| Kerb weight | kg | 2,377 |
| Payload | kg | 723-813 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 |
| Turning circle | m | 11.8 |
| Tank capacity and reserve | l | 57/10 |
| AdBlue® tank | l | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 10.1-10.2 |
| --- | --- | --- |
| Top speed | km/h | 203 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 6.7/ 5.7/ 6.1 |
| Efficiency class |  | A |
| CO2 emissions comb.1 | g/km | 161-160 |

Mercedes-Benz Marco Polo HORIZON 250 d 4MATIC

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 140 (190)/4,200 |
| Rated torque | Nm at rpm | 440/1,350-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | All-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

| Wheelbase | mm | 3,200 |
| --- | --- | --- |
| Track front/rear | mm | 1,670/1,650 |
| Length | mm | 5,140 |
| Width | mm | 1,928 |
| Height | mm | 1,995 |
| Kerb weight | kg | 2,445 |
| Payload | kg | 655-745 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 |
| Turning circle | m | 13.1 |
| Tank capacity and reserve | l | 57/10 |
| AdBlue® tank | l | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 11.1-11.2 |
| --- | --- | --- |
| Top speed | km/h | 196 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 7.4/ 6.3-6.2/ 6.7-6.6 |
| Efficiency class |  | A |
| CO2 emissions comb.1 | g/km | 176-175 |

Mercedes-Benz Marco Polo HORIZON 300 d

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 176 (239)/4,200 |
| Rated torque | Nm at rpm | 500 (+30)4/1,600-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | Rear-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

| Wheelbase | mm | 3,200 |
| --- | --- | --- |
| Track front/rear | mm | 1,666/1,646 |
| Length | mm | 5,140 |
| Width | mm | 1,928 |
| Height | mm | 1,995 |
| Kerb weight | kg | 2,377 |
| Payload | kg | 723-813 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 |
| Turning circle | m | 11.8 |
| Tank capacity and reserve | l | 57/10 |
| AdBlue® tank | l | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 8.3-8.4 |
| --- | --- | --- |
| Top speed | km/h | 215 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 6.7/ 5.7/ 6.1 |
| Efficiency class |  | A |
| CO2 emissions comb.1 | g/km | 161-160 |

Mercedes-Benz Marco Polo HORIZON 300 d 4MATIC

Engine

| Cylinder arrangement/number |  | R4 |
| --- | --- | --- |
| Displacement | cc | 1,950 |
| Bore x stroke | mm | 82.0 x 92.3 |
| Rated output | kW/hp at rpm | 176 (239)/4,200 |
| Rated torque | Nm at rpm | 500 (+30)4/1,600-2,400 |
| Emission class |  | Euro 6d-TEMP |

Power transmission

| Drive system |  | All-wheel drive |
| --- | --- | --- |
| Transmission |  | 9-speed automatic transmission (9G-TRONIC) |
| Gear ratios | 1. gear 2nd gear 3. gear 4. gear 5. gear 6. gear 7. gear 8. gear 9. gear Reverse gear | 5.35 3.24 2.25 1.64 1.21 1 0.86 0.72 0.6 4.8 |

Chassis

| Front axle | McPherson front axle with coil springs, stabilisers and shock absorbers |
| --- | --- |
| Rear axle | Semi-trailing arm rear suspension with coil springs, stabilisers and shock absorbers |
| Braking system | Disc brakes all-round, front brake discs internally ventilated, braking system with dynamic control systems, electronic stability programme ADAPTIVE ESP®, anti-lock braking system ABS, acceleration skid control ASR, Brake Assist BAS PRO, electronic brake force distribution EBV, electric parking brake |
| Steering | Electromechanical, speed-sensitive rack-and-pinion steering |
| Wheels | 6.5 J x 17 - 8 J x 19 |
| Tyres | 225/55 R 17 - 245/45 R 19 |

Dimensions and weights

| Wheelbase | mm | 3,200 |
| --- | --- | --- |
| Track front/rear | mm | 1,670/1,650 |
| Length | mm | 5,140 |
| Width | mm | 1,928 |
| Height | mm | 1,995 |
| Kerb weight | kg | 2,445 |
| Payload | kg | 655-745 |
| Permissible gross vehicle weight | kg | 3,100; 3,200 |
| Permissible trailer load unbraked/braked (at 12%) | kg | 750/2,000; 2,500 |
| Turning circle | m | 13.1 |
| Tank capacity and reserve | l | 57/10 |
| AdBlue® tank | l | 24 |

Performance and fuel consumption

| Acceleration 0-100 km/h | s | 9.0 |
| --- | --- | --- |
| Top speed | km/h | 210 |
| Fuel consumption (urban/extra-urban/comb.)1 | l/100 km | 7.4/ 6.3-6.2/ 6.7-6.6 |
| Efficiency class |  | A |
| CO2 emissions comb.1 | g/km | 176-175 |